## Slide 2: Module Objective
Upon completion of this module, participants will understand disaster search operations including geo-referencing, search definitions and search markings.

## Slide 3: Enabling Objectives
Understand and utilize the U.S. National Grid as a geo-referencing system for land SAR responders
Understand and utilize search strategies and definitions necessary in SAR operations
Understand and utilize standardized disaster SAR marking systems

## Slide 4: Unit 1
U.S. National Grid
(USNG)

## Slide 5: Terminal Objective
Upon completion of this unit, participants will be able to understand and utilize the U.S. National Grid as a point reference system to identify locations and document required information.

## Slide 6: Enabling Objectives
Successful participants will understand;
Importance of a single point reference system for all land SAR responders
U.S. National Grid as a geo-referencing system for land SAR responders
How to identify specific locations on a map
How to report and document required point reference locations

## Slide 7
“The USNG is intended to create a more interoperable environment … by establishing a preferred nationally-consistent grid reference system.”
CATASTROPHIC INCIDENT SEARCH AND RESCUE (CISAR) ADDENDUM
to the National Search and Rescue Manual
Version 1.1 (August 2008)

## Slide 8: CISAR Addendum & the USNG
AHJ may determine which geographic reference system will be used
Selected geographic reference system should be listed in the Incident Communications Plan (Form ICS 205)

## Slide 9: National SAR Committee CISAR Geo-referencing Matrix

## Slide 10: US National Grid Coordinate
What does the USNG Coordinate look like?

## Slide 11
GridZone
100k square
Easting (right)
Northing
(up)
Meters between 0-99,999
USNG Coordinate - Complete
14R NQ 82100 09500
Pre-Designated

## Slide 12: Grid Zone Designation (GZD)
14R NQ 82100 09500

## Slide 13: 100,000 Meter Square (regional area)
14R NQ 82100 09500

## Slide 14: USNG Accuracy
Accuracy is determined by amount of precision in coordinate (Easting and Northing)
Coordinate values represent a point position (southwest corner of grid square)
4 digits: 82 09 Identifies a point within a 1,000m square
(approx: 250 acres or 100 city blocks)
6 digits: 821 095 Identifies a point within a 100m square
(approx: football field)
8 digits: 8212 0952 Identifies a point within a 10m square
(approx: parking spot)- grid reader needed
10 digits: 82125 09525 Identifies a point within a 1m square
(approx: manhole cover)- GPS needed

## Slide 15: USNG Coordinate Communication
The USNG coordinate identifies both:
  Point Position: intersection of coordinate (most common)
  Area: grid square NE of point position
Users determine the required precision
The USNG coordinate can by truncated, i.e.:
“821 095” instead of “82100 09500“
GPS devices require full coordinate string

## Slide 16: Read RIGHT (Easting)  then UP (Northing) 
14R NQ 82100 09500
1,000 meter accuracy
(4 digits)
This point identifies the USNG coordinate
Grid square (1000m x 1000m), up and right of coordinate

## Slide 17: Read RIGHT (Easting)  then UP (Northing) 
14R NQ 82100 09500
100 meter accuracy (6 digits)

## Slide 18: Read RIGHT (Easting)  then UP (Northing) 
14R NQ 82100 09500
10 meter accuracy (8 digits)

## Slide 19: USNG in Disaster Response
Can be used to assign areas of responsibility without defined boundaries
  tasking to ‘search proximity’ around coordinate
Coordinate point position can define:
Survivor location
Base of Operations
Address of significance
Landing Zone (LZ)
Survivor Collection Point
Hazards
Vehicle location
Other?

## Slide 20
right
What is the major feature at grid coordinate 13 09?
  4 digits (2x2): 1,000m accuracy
  Grid Square is approx. ½ mile in length or approx. 250 acres
  GPS would report this coordinate as 16R BU 13000 09000
11
09
10
11
10
09
up
Mississippi River
13 09

## Slide 21
Could 125 098 be used as a potential Landing Zone (LZ)?
  6 digits (3x3): 100m accuracy
  Grid Square is approx. length of football field
  Leading zero is needed (GPS would report this as 16R BU12500 09800)
11
09
10
11
10
09

## Slide 22
Would you require a Hazmat check before searching grid coordinates 145 099?
  6 digits (3x3): 100m accuracy
  Grid Square is approx. length of football field
  GPS would report this coordinate as 16R BU 14500 09900
11
09
10
Tulane University Research Laboratories
11
10
09

## Slide 23
What is the 6 digit grid coordinate for Channel Light 18?
  6 digits (3x3): 100m accuracy
  Grid Square is approx. length of football field
  GPS would report this coordinate as 16R BU 13500 09800
135 098
11
09
10
11
10
09

## Slide 24
What is the 6 digit grid coordinate for the water tank?
  6 digits (3x3): 100m accuracy
  Grid Square is approx. length of football field
  GPS would report this coordinate as 16R BU 12500 10800
125 108
11
09
10
11
10
09

## Slide 25
Is there potentially shelter available 360 meters to the Southeast of the water tank?
What is the coordinate for that location?
  What would a GPS report for this coordinate?
1000 meters
11
09
10
11
10
09
128 106
16R BU 12800 10600

## Slide 26: Summary
Multiple SAR agencies used a variety of geo-referencing systems during Hurricane Katrina, causing confusion.
USNG geo-referencing scheme is to be used when a Catastrophic Incident is declared as outlined in the National Response Framework (January, 2008).
Additional information and training concerning the USNG can be found online. http://www.fgdc.gov/usng

## Slide 27: Unit 2
Search Definitions and Standards

## Slide 28: Terminal Objective
Upon completion of this unit, participants will be able to understand and utilize the search strategies and definitions necessary to accomplish the assigned search and rescue objectives.

## Slide 29: Enabling Objectives
Successful participants will understand:
  Standard search definitions
  Search modes
  Phases of disaster search operations

## Slide 30: Recon
Structured and organized survey
Preliminary and cursory check of an area
Immediate and continuous
Incident driven and flexible
Timely reporting of information

## Slide 31: Recon Methods
Air
  Helicopter
  Fixed wing
  Satellite imagery
Water
Windshield survey

## Slide 32: Purpose of Recon
Determine scope and magnitude of incident
Identify resources needed
Record victim location
Request rescue resources

## Slide 33: Recon Team Configuration
Incident driven
Small
Mobile
Flexible
Inconspicuous (where possible)

## Slide 34: Psychology of Recon
Recon is a state of mind
  Do the most good for the most people
  First snapshot of entire event
  Drives the response effort
Recon is triage…NOT search or rescue!

## Slide 35: Hasty Search (Rapid)
Fast-paced search to locate and remove lightly-trapped survivors with available equipment
  survivors moved to collection points
Additional resources called for survivors unable to be removed while search continues
Documentation of areas searched and finding must be recorded and reported

## Slide 36: Primary Search
Quick search of structures likely to contain victims…looking in, not going in
May include physical, canine and technical
Additional resources called for trapped survivors while search continues
May perform actions necessary to immediately correct life threatening injuries
Survivor and/or human remains locations marked with standard marking systems

## Slide 37: Secondary Search
Systematic search of every area of every structure
May involve extensive debris removal
  Low Coverage: search void spaces
  High Coverage: complete de-layering
Additional resources called for trapped survivors while search continues
Survivor and/or human remains locations marked with standard marking systems

## Slide 38
Recon
Hasty
Primary
Secondary
SEARCH
SEARCH

## Slide 39: Special Response Team
Deployed to investigate pre-identified facilities that are likely to require evacuation assistance
Hospitals
Nursing Homes
Evacuation Shelters
Critical Infrastructure Facilities
Areas of last refuge such as fire stations and police precincts

## Slide 40: Remember! The AHJ has the authority to modify these definitions.
Modifications must be clearly stated.
Search definitions must be made available to all team members assigned to the incident.

## Slide 41: Other SAR Terms
Structural Collapse SAR
Wide Area SAR
Evacuation
Extraction
Extrication
Detection
Location

## Slide 42: Search Phases
I | Recon | Intelligence gathering
II | Hasty | Surface survivors removed and evacuated
III | Primary | Searching accessible voids that may contain survivors
IV | Secondary | Selected debris removal. Extended operations required to extricate survivors
V | Search completed | General debris removal

## Slide 43: Summary
Understanding and utilizing the search strategies and standard definitions is necessary to accomplish the assigned search and rescue objectives.

## Slide 44: Unit 3
Search Marking Systems

## Slide 45: Terminal Objective
Upon completion of this unit, participants will be able to understand and utilize standardized disaster search and rescue marking systems.

## Slide 46: Enabling Objectives
Successful participants will understand and be capable of utilizing the follow standardized disaster marking systems:
Grid and Block Marking System
Structure Hazard Evaluation Marking System
Structure/Hazard Marking System
Survivor and Human Remains Marking Systems

## Slide 47: Grid and Block Marking
Use existing hundred block. Even numbers on one side, odd numbers on other side
Mark new numbers on the front with orange spray paint.
Street not identifiable, start with the letter “A” using the phonetic alphabet “Alpha”, “Bravo”, Charlie, etc.

## Slide 48
701
706
702 704 708 710
703 705 707 709
700 block of Alpha St

## Slide 49: Side and Floor Identification
Street side is ‘A’. Rotate clock-wise
SIDE C
SIDE A
SIDE
D
SIDE
B
700 Block Alpha Street
Multi-story structures
    Ground floor: Floor 1
    Second Story: Floor 2
    Basement, floors below ground: B-1

## Slide 50: Structure Markings
15JUN92
HM NATURAL GAS
OR–1
HM
Structure relatively safe
Structure is significantly damaged
Structure is not safe
Arrow indicates direction of safest entry
Hazardous materials in or near the structure
Copyright 2009 FEMA

## Slide 51: Search Markings—Elements
Search team identifier
Date of entry
Time of entry
Date and time search team left structure
Hazards
Total victims STILL INSIDE the structure

## Slide 52: Search Markings— Example of a Completed Search
Search Team Identifier
Date of Entry
Time of Entry
Date & Time Search Team Left the Structure
Hazards
Total Number of Victims STILL INSIDE the Structure
Copyright 2009 FEMA

## Slide 53: Search Markings— Example of a Completed Search
2/24
1520 hrs
Natural Gas
2 L
3 D
TX-TF1 2/24/08 1150 hrs

## Slide 54: Search Markings Initial Entry
TX-TF1 2/24/08 1150 hrs
Required Information
What it Looks Like
Search Team Identifier Date of Entry Time of Entry
Notes: 53

## Slide 55: Search Markings Incomplete Search
Required Information
What it Looks Like
Search Team Identifier Date of Entry Time of Entry
Date and Time Search Team Exits Structure
Hazards Found in the Structure
Total Victims Still Inside the Structure
Areas Completed
Additional Information
2/24
1520 hrs
Natural Gas
2 L
3 D
TX-TF1 2/24/08 1150 hrs
Floor 1–6
Gas on F7
Notes: 54

## Slide 56: Peel and Stick

## Slide 57
Search Sticker on concrete building.
Note the additional information in the box below the search ‘X’.

## Slide 58: Interior Search Markings (each room or area)
When you ENTER
When you EXIT
Identify any victims
Identify any hazards

## Slide 59: Survivor Markings
SMA
6’
SMA
2
SMA
3
SMA
Potential survivor and team identifier
Confirmed and alive; If more than one survivor, place number below V
Confirmed and deceased; If more than one confirmed human remains, place number below V
Person has been removed
Point toward victim with distance on arrow

## Slide 60
Exit
Entry
Empty
CA
6
Water
Water
1 - L
2 - D
CA-6
1-12
1300
Water
1-L
2-D
1-12
1500
CA
6
CA
6
Source Unknown

## Slide 61: Summary
SAR responders must have uniform standardized system for marking buildings or other structures to indicate the status of searched structures.
Having a common search marking system reduces the possibility of redundant searches.